## Slide 1: AIR COMPRESSOR REVERSE ENGINEERING
Nathan Owen Santoso, Terry Lao, Zoe Hughes, Muhammed Ahmed, Cheuk Yui Chong

## Slide 2: CONNECTING ROD

## Slide 3: FUNCTION
http://www.technologystudent.com/cams/crkslid1.htm
Connects crankshaft to piston base
Rotational motion
Reciprocal motion


## Slide 4: MATERIAL
Cyclic stresses
Prone to fatigue failure
Transfer of motion
Minimal plastic/elastic deformation
∴ Not polymer
Critical component
Catastrophic failure unfavourable
Ductility preferred
∴ Not ceramic
Visual resemblance
Silver coloured
Metallic finish
∴ Metal
∴ High strength

## Slide 5
http://autocomponentsindia.com/shree-jay-jagdamba-stainless-steel-plans-expansion-in-capacity-products/
https://www.admiralmetals.com/products-services/carbon-steel-12l14-2/
STAINLESS
steel
CARBON
steel

## Slide 6: MANUFACTURING
Steel cut into billets
Heated to ~1300C
Impression die forging
Machining
http://www.steadfastfze.com/images/steel_hot_billets_rod.jpg
https://i.ytimg.com/vi/hoD6gzUHpns/maxresdefault.jpg
https://image.made-in-china.com/202f0j00AFCtjiOEfDqf/Cold-Drawn-Small-Steel-Billet-Various-Shape.jpg
http://s177546276.onlinehome.us/Images/forging_impression-Final.gif

## Slide 7: COUNTERWEIGHT

## Slide 8: Function
Provides Balance and stability
Increases efficiency
Saves energy
Allows movement with lower driving forces
Reduces vibrations allowing the system to rotate smoothly

## Slide 9: Material & Properties
Most likely a steel alloy
Close to the budget range (low cost raw material)
Relatively dense
Corrosion of the steel can be prevented by paint coating (cost-effective)
High strength and hardness
http://www.hvsteel.com/SiteFiles/hvsteelcomau/content-banner-tubular-steel-pipes.jpg

## Slide 10: Manufacturing
Die Casting (Hot chamber, Zinc)
Steel mold is sprayed with a lubricant:
  Regulates temperature
  Easier to remove the cast
Liquefied metal transferred to die through extreme pressure
Mold cooled by immersing or sprayed with cold water
Cast removed
Less metal scraps
Very efficient production with excellent accuracy
http://aarne.co.uk/wp-content/uploads/2017/07/Bronze-Casting.jpg

## Slide 11: CIGARETTE LIGHTER PLUG HOUSING

## Slide 12
Act as an insulator
Acid, heat and impact defence
Prevent slipping
Slight water-proofing
FUNCTION
Hard Rod Shape

## Slide 13
Function | Material properties
Insulating | PVC – Good insulator – No free electrons PVC – Not subject to electrolysis / current corrosion
Acid, heat, impact defence | PVC – Hard – High density polymer chain. PVC – High melting point PVC – Stable – Acid resistance
Protect users | PVC – Thermoplastic – softening if overheated
MATERIAL PROPERTIES

## Slide 14: MANUFACTURING
Melt the raw plastic
Fill the injection unit with molten plastic
Inject the plastic to the mold
Apply force to hold the mold
Solidify while cooling
Ejection (with mold release agents)
Trimming
http://www.custompartnet.com/wu/images/im/injectionMolding_machine_overview.png

## Slide 15: FUSE

## Slide 16: function
Safety feature to prevent overloading of circuit
https://image1.masterfile.com/getImage/Njk2LTAzMzk4ODEyZW4uMDAwMDAwMDA=AHetM6/696-03398812en_Masterfile.jpg

## Slide 17: material properties
Element: (Zinc or aluminium alloy)
Conduct electricity
Low melting point
Ductile
Casing: (Glass)
High yield strength
Electrical Insulator

## Slide 18: MANUFACTURING
Element
Drawing – process in which the diameter of a stock piece of metal is reduced
Glass
Danner process: molten glass is formed into a tube using a rotating mandrel
Annealing – reduces internal stress in the wire to improve its metallic properties

## Slide 19: POWER CABLE

## Slide 20: Function
Electrical connection to the power supply
Thermal and electrical insulation
Connection to power supply from fair distances

## Slide 21: Material
Conducting Material (Copper)
- Cheap, ductile and easily available
- High melting point with low resistivity
- High purity
Insulating Material (PVC)
- Good thermal and electrical insulator
- Flexible
- Cheap and available in bulk quantity
- Ability to withstand frequent wear and tear

## Slide 22: Manufacturing
First
- Reduction of diameter of wire
- Increase in its ductility and conductivity
Second
- Annealing
- Removal of internal stresses
- Increase in conductivity
Third
The wire is insulated
- Increase in toughness

## Slide 23: bibliography
‘Forging vs Casting’, Compass & Anvil, [website], 2012, https://www.compass-anvil.com/forging-vs-casting, (accessed 25 Aug. 2018)
‘Hot Forging of Connecting Rod’, CFS Steel Forging, [website], 16 June 2018, http://www.steelforging.org/hot-forging-of-connecting-rod/, (accessed 26 Aug. 2018)
Duan, M., ‘How to Forge the Connecting Rod’, LinkedIn, [web blog], 28 June 2017, https://www.linkedin.com/pulse/how-forge-connecting-rod-michael-duan, (accessed 25 Aug. 2018)
Greenhaw, E., 'How An Electrical Cable Is Made', ECNMAG, [website], 2016, https://www.ecnmag.com/blog/2016/04/how-electrical-cable-made (accessed 2 Sept. 2018)
Fuses: Chapter 12 - Physics of conductors and insulators, [website], https://www.allaboutcircuits.com/textbook/direct-current/chpt-12/fuses/, (accessed 26 August 2018)
Metal Casting Process, [website], https://thelibraryofmanufacturing.com/metalcasting_basics.html, (accessed 26 August 2018)
Steel material properties, [website], https://www.steelconstruction.info/Steel_material_properties, (accessed 27 August 2018)
Wiley, J. Fundamentals of Modern Manufacturing, [website], 2002, http://www.me.nchu.edu.tw/lab/CIM/www/courses/Manufacturing%20Processes/Ch12-Glassworking-Wiley.pdf, (accessed 27 August 2018)
Tube Glass: Danner Process, [website], https://www.eurotherm.com.au/tube-glass, (accessed 27 August 2018)
‘Everything you Need to Know About PVC Plastic’, Creative Mechanisms, [web blog], 6 July 2016, https://www.creativemechanisms.com/blog/everything-you-need-to-know-about-pvc-plastic, (accessed 20 Aug. 2018)
‘Injection Molding’, Custompartnet, [website], 2007, http://www.custompartnet.com/wu/InjectionMolding, (accessed 20 Aug. 2018)
‘Counterweights information’, IEEE Global Spec, [website], https://www.globalspec.com/learnmore/mechanical_components/industrial_hardware/counterweights, (accessed 3 Sep, 2018)
‘Die Casting vs. Injection Molding: Pros and Cons’, National molding, [website], https://nationalmolding.com/blog/die-casting-vs-injection-molding-the-pros-and-cons/, (accessed 3 Sep. 2018)
‘Die Casting’, Dynacast International Inc, [website], https://www.dynacast.com/die-casting, (accessed 3 Sep. 2018)