## Slide 1: Preliminary Design – Battery Monitor IC & Microcontroller Interface
Owen Santoso (22466085), Project Administrator - Risk
ELEC5552 - Team 06, 31/08/2022

## Slide 2: Role & Responsibilities
Project Administrator – Risk
  Create and maintain Risk Register (D22#00006R1)
  Update with any risks that the team identifies during the project
Requirements Analysis
  Contributed to Executive Summary, State of Charge Literature Review section, Adding requirements from information sessions, Proofreading

## Slide 3: BQ76942 ↔ Microcontroller Interface

## Slide 4: BQ76942 Communication Types
Supports communications options of
  I2C
  HDQ
  SPI
We will use SPI to keep consistent with primary-secondary board communication type

## Slide 5: BQ76942  Microcontroller

## Slide 6: BQ76942  Microcontroller
Main
BQ76942
Subnode
K

## Slide 7: BQ76942  Microcontroller
Main
BQ76942
Subnode
K

## Slide 8
✓
✓
✓
Need to change
config
Default Communication Configuration
BQ76942 defaults to either I2C or SPI depending on version
Need to check what version when we order

## Slide 9: Changing Communications Type
The Settings:Configuration:Comm Type register determines the communication type
‘Default’ may be different depending on device version
We will set this register to 0x10 for SPI with CRC for error detection (ENV_6)

## Slide 10: Register Addresses
Register addresses can be found from the Data Memory Table in pg. 196 of Technical Reference Manual
Address of Comm Type register is 0x9239
…

## Slide 11
Primary board will request data every 1 second to secondary board microcontroller
Microcontroller will request data from the BQ76942 IC when it receives primary board request
BQ76942 will send the data to the microcontroller
Microcontroller will send this data back to the primary board using the daisy chain SPI communication
Data Collection

## Slide 12: Subcommands
BQ76942 supports subcommands, which are 2 bytes rather than normal 1 byte commands
Can query multiple data values from the chip in one subcommand, rather than sending multiple commands
Subcommands table found on pg. 110 of Technical Reference Manual

## Slide 13: Example Code
Texas Instruments also provides example code on their website for both I2C and SPI communication types
Includes header files which define many of the addresses required

## Slide 14: Questions